## Slide 2: How Much Power Must We Extract From a Receiver Antenna to Effect Communications?

## Slide 3
Evaluating the Necessity of Power Extraction in
Receiver Antennas via Gradient Descent
Optimization
Vũ Nguyễn Anh Tuân 202417212
Nguyễn Phan Vĩ 202417218
Phan Công Trường Sơn 202417190
Phạm Huy Khánh 202417137

## Slide 4: Table of contents
Overview of the original paper
Optimization objectives and method
Obtained results
Conclusions

## Slide 5
Overview of the original paper

## Slide 6: Paper’s goals:
Challenge the common technical assumptions and practices that power extraction as essential
Highlight the distinction between what is physically mandatory and what is merely a convenience in design

## Slide 7: Summary
Rejects the notion that extracting power from a receiver antenna is imperative
Shannon information theory is purely mathematical and does not represent the physical world
Presents amplifier circuits capable of measuring the open-circuit voltage without extracting power
Impedance matching does not necessarily result in optimized SNR value
Noise figure is merely a standard definition and is not a physical principle
Impedance matching and power extraction can sometimes be used advantageously to obtain noise-free voltage gain prior to the preamplifier, but is impractical
Suggests applying lessons learned to broad-band receiver antenna arrays and possible advantages of measuring open-circuit voltages on the antenna ports as opposed to drawing current from the antennas

## Slide 8: Paper’s conclusion
How much power must we extract from a receiver antenna to effect communications?
Answer:
Subject to the laws of classical physics:
None!

## Slide 9
Optimization objectives and method

## Slide 10: Objectives
  Maximize the signal-to-noise ratio (SNRo) relative to the complex antenna impedance (ZR) and complex load impedance (ZL)

## Slide 11: Objectives
  Maximize Friis gain (G)

## Slide 12: Objectives
  Maximize the signal-to-noise ratio (SNRo) relative to the source resistance (RS) and the load resistance (RL)

## Slide 13: Objectives
  Maximize output signal voltage (Vso) relative to the source resistance (Rs) and the load resistance (RL)

## Slide 14: Objectives
  Maximize output signal power (Pso) relative to the source resistance (Rs) and the load resistance (RL)

## Slide 15: Objectives
  Minimize the output signal’s noise power (Pno) relative to the source resistance (Rs) and the load resistance (RL)

## Slide 16: Objectives
  SNRo: retain signal integrity for decoding
  G: maximize signal strength
  Vso, Pso: obtain the strongest output signal
  Pno: retain signal integrity

## Slide 17: Optimization method
  Gradient Descent:

## Slide 18: Optimization method
  Gradient Descent: Limitation – Vanishing Gradient
  Maximization problem => optimize
  algorithm stops prematurely
  Solution:
  Adam Optimizer

## Slide 19: Optimization method
  Adam Optimizer:
  Momentum: accumulates past gradients
  : The exponential decay rate for the first moment estimates (momentum)
  Adaptive step sizes => faster time to extrema

## Slide 20: Optimization method
  Adam Optimizer:
  Exponentially decaying average of past squared gradients
  : The exponential decay rate for the second moment estimates (variance)
  Bias correction (zero bias)
  First moment:
  Second moment:

## Slide 21
Obtained results

## Slide 22: Obtained results
SNRo (equation 9):
ZR:
  Real bound: [10; 1500]
  Imaginary coefficient bound: [-1500; 1500]
ZL:
  Real bound: [10; 1500]
  Imaginary coefficient bound: [-1500; 1500]
Other parameters:
  g: 10
  Nna: 1e-9
  k: 1.38e-23
  T: 300
  SIT: 1.26e-4
  => Obtained value: 91.48 dB at
  ZR = 10 + 1500j
  ZL = 10 - 1500j

## Slide 23: Obtained results

## Slide 24: Obtained results
SNRo (equation 9):
  Real bound: [0.01; 1e9]
  Imaginary coefficient bound: [-1500; 1500]
Other parameters:
  g: 10
  Nna: 1e-9
  k: 1.38e-23
  T: 300
  SIT: 1.26e-4
  => Obtained value: 53.98 dB at
  ZR = 0.01 + 1352.14j
  ZL = 1e9 + 295.98j

## Slide 25: Obtained results

## Slide 26: Obtained results
G (equation 18):
Rs ∈ [0.01, 1e6]
RL ∈ [0.01, 1e9]
Other parameters:
Other parameters:
  g: 10
  Rs: 50 Ω
  Optimal Gain: 63.00 dB | Rs = 1000000.00 Ω | Rl = 1000000000.00 Ω

## Slide 27: Obtained results

## Slide 28: Obtained results
G (equation 18):
Rs = 100 Ω
RL ∈ [0.01, 1e9]
Other parameters:
Other parameters:
  g: 10
  Rs: 50 Ω
  Optimal Gain (Fixed Rs): 23.01 dB | Rl = 1000000000.00 Ω

## Slide 29: Obtained results

## Slide 30: Obtained results
SNRo (equation 20):
Rs ∈ [0.01; 1e6]
RL ∈ [0.01; 1e9]
Other parameters:
  Vs = 1.0 V
  T = 300.0K
  Nna = 1e-12 W/Hz
  k = 1.38e-23 J/K
  g = 10.0
  Obtained value: 140.00 dB at
  Rs = 0.01Ω and RL = 1e9Ω

## Slide 31: Obtained results

## Slide 32: Obtained results
Vso (equation 17-1):
Rs ∈ [0.01; 1e6]
RL ∈ [0.01; 1e9]
Other parameters:
  Vs = 1.0 V
  g = 10.0
  Obtained value: 10V at
  Rs = 0.01Ω and RL = 1e9 Ω

## Slide 33: Obtained results

## Slide 34: Obtained results
Pso (equation 17-2):
Rs ∈ [0.01; 1e6]
RL ∈ [0.01; 1e9]
Other parameters:
  Vs = 1.0 V
  g = 10.0
  Ro = 50Ω
  Obtained value: 0.5 W at
  Rs = 0.01Ω and RL = 1e9Ω

## Slide 35: Obtained results

## Slide 36: Obtained results
Pno (equation 19):
Rs ∈ [0.01; 1e6]
RL ∈ [0.01; 1e9]
Other parameters:
  Ro = 50Ω
  T = 300.0K
  Nna = 1e-12 W/Hz
  k = 1.38e-23 J/K
  g = 10.0
  Minimum Pno: 5.0000e-15 W | Rs = 0.01 Ω | Rl = 950714306.39 Ω

## Slide 37: Obtained results

## Slide 38
Conclusions

## Slide 39: Conclusions
From (9), while impedance matching result in an optimized SNR, it is limited to a specific reactance, meaning broadband is not supported
From the obtained results of eq 18, to achieve the maximum signal voltage, we should connect the antenna (the source) to an amplifier with an infinite input impedance (an open circuit). This is equivalent to drawing no current or power from the antenna.
Obtained results directly challenges the conventional wisdom that there must be power transfer (i.e., there must be current and a finite load) for the amplifier to operate effectively

## Slide 40
THANK YOU !